## Slide 1
ECE-249
Unit-2
Fundamentals of A.C. circuits
.

## Slide 2: Contents:
2
Alternating Current
Generating Ac Voltages
Determination of Frequency (f) In The Ac Generator Fundamental
Periodic Voltage Or Current Waveform
  Average Value
  Root Mean Square (RMS) Value
  Average And RMS Values Of Sinusoidal Voltage Waveform
Single-phase AC Supply
  Purely Resistive Circuit (R Only)
  Purely Inductive Circuit (L Only)
  Purely Capacitive Circuit (C Only)

## Slide 3: Cont:
3
series A.C. circuit
  R–L series A.C. circuit
  R–C series A.C. circuit
  R–L–C series A.C. circuit
Three-phase AC Circuits
  Generation of Three-phase Balanced Voltages
  Delta(Δ)-Star(Y) conversion and Star-Delta conversion
  Delta(Δ)-Star(Y) conversion and Star-Delta conversion impedance conduction

## Slide 4
AC Fundamentals
Previously you learned that DC sources have ﬁxed polarities and constant magnitudes and thus produce currents with constant value and unchanging direction
In contrast, the voltages of ac sources alternate in polarity and vary in magnitude and thus produce currents that vary in magnitude and alternate in direction.

## Slide 5: Generating AC Voltages
Generators convert rotational energy to electrical energy.
Generate alternative emf by rotating a coil within a stationary magnetic field.
Another way to rotating magnetic field a within a stationary coil.
5

## Slide 6: Cont….
The armature has an induced voltage, which is connected through slip rings and brushes to a load.
The armature loops are wound on a magnetic core
6

## Slide 7
7
A multi-turn coil is placed inside a magnet with an air gap as shown in above Fig.
The flux lines are from North Pole to South Pole. The coil is rotated at an angular speed,
ω = 2 π n (rad/S)
N is rotating a rectangular coil in a counter clockwise direction with a angular velocity of ω radians per sec in a uniform magnetic field.
The instant of coincidence of the plane of the coil with X-axis. At this
instant max flux, link with the coil
  The coil assume the position, as shown in fig , after moving the counter clockwise for t sec.
  The angle ө through which the coil has rotated
in sec = ω t.

## Slide 8
The component of flux along perpendicular to the coil = Φmax Cos ωt.
Flux linkage of the coil at the instant = no. of turns on coil x linkage flux
N Φmax Cos ωt
emf induced in a coil is equal to the rate of change of the flux linkage with minus sign .
emf induced is max at any instant.
Instantaneous emf , e = Emax sin ωt
8
8

## Slide 9: .A way to provide high efficiency, safe low voltage:
High Voltage Transmission Lines
Low Voltage to Consumers
05-10-2021
9
step-up to 500,000 V
step-down,
.back to 5,000 V
step-down to 120 V
~5,000 Volts

## Slide 10: Periodic Voltage or Current Waveform
Average value
  The current waveform shown in Fig, is periodic in nature, with time period, T. It is positive for first half cycle, while it is negative for second half cycle.
  The average value of the waveform, i(t) is defined as
In this case, only half cycle, or half of the time period, is to be used for computing the average value, as the average value of the waveform over full cycle is zero (0).
If the half time period (T/2) is divided into 6 equal time intervals (TΔ)

## Slide 11: Root Mean Square (RMS) value
For this current in half time period subdivided into 6 time intervals as given above, in the resistance R, the average value of energy dissipated is given by
Heat produce during interval =
jouless

## Slide 12: Average Values of Sinusoidal Voltage Waveform
The average value of sine wave over the complete cycle is zero.
The half wave value of sinusoidal current is
For half cycle when ωt varies from 0 to π
Similarly

## Slide 13: RMS Values of Sinusoidal Voltage Waveform
The waveform of the voltage v(t), and the square of waveform, , are shown in figures 12.4a and 12.4b respectively.
Similarly for current RMA value

## Slide 14: Form factors
The form factor of an alternating quantity is define as the ratio of RMS value to the average value.
Peak value:-
The peck factor of an alternating quantity is define as the ratio of maximum value to the average value
NOTE:-
  The rms value is always greater than the average value.
  Except for a rectangular waveform, in which case the heating effect
remains constant, so that the average and the rms values are same

## Slide 15: Question
Q1) determine the average value and RMS value of sinusoidal current
of peak value 40A.
Solution:- Imax = 40A
Q2) write the instantaneous value for a 50Hz sinusoidal voltage supply
for domestic purposes at 230V.
Solution:- given value Vrms = 230 V. , f = 50 Hz

## Slide 16: Single-phase AC Supply
Purely resistive circuit (R only)
  The instantaneous value of the current though the circuit is given by
Im and Vm are the maximum values of current and voltage respectively

## Slide 17: Purely inductive circuit (L only)
For the circuit , the current i, is obtained by the procedure described here
⚫

## Slide 18: Purely capacitive circuit (C only)

## Slide 19
From our earlier discussions we know that
where Vm is the peak voltage
 is the angular frequency
 is the phase angle
Since  = 2f it follows that the period T is given by
T  1  2
f 
If  is in radians, then a time delay t is given by  / as shown
below

## Slide 20
Sinusoidal signals are characterised by their magnitude, their frequency and their phase
Amplitude
Phase angle
Angular or radian frequency = 2f = 2/T
Period = 1/f

## Slide 21
21
21
Example
v
i
Circuit element
+
v
_
i
The voltage lags the current by  radians.
05-10-2021
Voltage and current of a circuit element.
The current leads the voltage by  radians.
OR
cos  sin    
 2 


sin  cos   
 2 
 

## Slide 22: Mathematical representation of phasor
Phasor can be representation in two way.
  Rectangular form
  Polar form
Polar form:-
For example v(t) = 20 sin(2πft + 60).
  Then it represented in the polar form
The instantaneous voltagevs
represented in polar form.
 Vm sin t   can be

## Slide 23
can be
represented in Rectangular form.
v(t) = x + jy
Where 'x‘ is x component of the phasor = Vm cos φ
‘y' is y component of the phasor = Vm sin φ
V(t) = Vm cos φ + j Vm sin φ
Example: v(t) = 20 sin(2πft + 60).
v(t) = 20 (cos 60 + j sin 60). = (10 + j17.32)
For Rectangular form:-
  The instantaneous voltagevs
 Vm sin t   

## Slide 24
= r sin φ
Conversion from polar to rectangular:
  Polar form :
For x component x = r cos φ and y component y
v(t) = x + jy
V(t) = r cos φ + j r sin φ
Conversion from rectangular to polar :
  For rectangular form v(t) = x + jy
For polar form
=

## Slide 25
Phasor Relationship for R, L, and C Elements
Time domain
v  Ri
R
Frequency domain
V  RI or I  V
Resistor
Voltage and current are in phase.

## Slide 26: Inductor
Time domain
Frequency domain
v  L di
V  jLI
or I  V   jV
jL L
dt
Voltage leads current by 90
Current lags voltage by 90

## Slide 27: Capacitor
Time domain
Frequency domain
I   jI jC C
I  jCV or V 
dv dt
i  C
Voltage lags current by 90
Current leads voltage by 90

## Slide 28: Impedance and Admittance
magnitude Z
or
Z  Z 
polar
28
 Ze j
exponential
 R  jX
rectangular
Impedance is defined as the ratio of the phasor
voltage to the phasor current.
Ohm’s law in phasor notation
phase    

## Slide 29: Graphical Representation of Impedance Z  Z 
R2
Z   X 2
R
  tan1 X
Resistor
Inductor
Capacitor
Z  R
Z  jL
1   j jC C
Z 
R
L
C

## Slide 30
Admittance is defined as the reciprocal of impedance.
1

1
Z Z 
In rectangular form
1
R2
R  jX

 G  jB
X 2
Y  1 
Z R  jX
 Y   
conductance
susceptance
Resistor
Inductor
Capacitor
1
R
Y  G 
1
j L
Y 
Y  jC
L
C
G
In Polar form
Y 

## Slide 31: AC circuit with series element
The series R-L Circuit
  We consider the ac circuit consisting of resistance of R and inductance of L
connecting in series.
V = VR + VL
VR = I R VL = I XL
V = I R + I XL
where XL = ωL = 2πf L
Vector sum of the VR and VL

## Slide 32: Impedance of R-L series circuit
Impedance of R-L series circuit is expressed in the rectangular form as
  Z = R + j XL
Expressed in the polar form as
Expression for current:
  The current through the R-L circuit is
i(t) = Im Amp.
instantaneous current i(t) = Im sin (ωt - 𝜙)

## Slide 33: Power in Resistance - inductance circuit
Instantaneous power,
33
Since average value of pulsating component
over the complete cycle is zero.
  The average power of the circuit
V & I are the RMS value of voltage & current and φ is the phase angle between applied voltage & current.

## Slide 34: The series R-C Circuit
We consider the ac circuit consisting of resistance of R and inductance of L connecting in series
34
Voltage drop across R , VR = I R
⚫
(VR is in phase with I)
Voltage drop across C , Vc = I Xc
⚫
(VC lags I by 90)
Applying KVL for RC series circuit
V = VR + Vc
= I XC
where XC = 1/ωL = 1/2πf C
VR = I R and VC V = I R + I XC
Vector sum of VR
and VL

## Slide 35: Impedance of R-C series circuit
3535
Impedance of R-C series circuit is expressed in the rectangular form as
  Z = R - j XC
Expressed in the polar form as
Expression for current:
  The current through the R-L circuit is
i(t) = Im Amp.
instantaneous current i(t) = Im sin (ωt + 𝜙)

## Slide 36: Series R-L-C Circuit
36
C
I
C C
  90
A Phasor Diagram is a graphical representation of phasors and
their relationship on the complex plane.
The voltage phasors are
VR  RI  RI0
VL  jLI  LI90
V   j I 
Vs  VR  VL  VC
Applied voltage V, being equal to the phasor vector sum of VR, VL & VC
is given in magnitude

## Slide 37: Three-phase System

## Slide 38
Single phase generator
38
Three phase generator

## Slide 39: Three-phase AC Circuits
Generation of Three-phase Balanced Voltages
  Three windings, with equal no. of turns in each one, are used, so as to obtain equal voltage in magnitude in all three phases.
  Also to obtain a balanced three-phase voltage, the windings
120 with each
40
are to be placed at an electrical angle of
other.
Contraction:-
consider three identical coil “a1a2”, “b1 b2”, and “c1c2” are mounted in same axis but displaced from each other by 120 rotating in counter clockwise direction in bipolar magnetic field as shown in fig.

## Slide 40
05
-10-2021
41
When a coil “a1 a2” is the position AB the induced emf in this coil is zero.
At that time ‘b1 b2’ is 120 behind the coil ‘a1 a2’ so the emf is induced in this coil as approaching its maximum negative (-ve) value .
At the same time ‘c1 c2’ is 240 behind the coil ‘a1 a2’ so the emf is induced in this coil as approaching its maximum positive (+ve) value and is decreasing

## Slide 41
42
Some important point
The induced emf in each of the coil are of same magnitude.
The induced emf in each of the coil are of same frequency and Waveform (sinusoidal wave).
The instantaneous value of the emf induced in the coil “a1 a2” , “b1 b2” and “ c1 c2”is given as below.
Note:- if t = 0 corresponding to the instant then voltage & emf of the coil “a1 a2” pass through zero & increasing in positive
05-1d0i-2r0e2c1tion.

## Slide 42: Balance Three Phase Star Connection
The connection diagram of a star (Y)-connected three-phase system is shown in Fig.
Three phase voltages (EP) are:
Three line voltages (EL) are:
  ERY
  ERB
  EYB

## Slide 43: Phase Representation of Star Connection

## Slide 44: Relation between Phase and Line Voltages for Star Connection
Three line voltages are obtained by the following procedure. The line voltage, ERY is
The magnitude of the line voltage, is ERY is times the magnitude of the phase voltage ERN.
ERY lead the ERN by 30 degree

## Slide 45: Cont…
Similarly other line voltages EYB as shown in brief
times the
The magnitude of the line voltage, is EYB is magnitude of the phase voltage EYN.
ERY lead the ERN by 90 degree
Similarly other line voltages EYB as shown in brief
So, the three line voltages are balanced, with their magnitudes being equal, and the phase angle being displaced from each other in sequence by 30.

## Slide 46: Relation between the Phase and Line Current for Star Connection
In the star connected system each line connector is connected to separate phase, so current flowing through the lines and phase
  Lines Current IL (IRY, IRB, IYB) = Phase Current IP (IBN, IYN, IRN)
If the phase current has a phase difference of φ with the phase voltage, then
  Power output per phase = EP IP cosφ
  Total power output phase = 3 EP IP cosφ

## Slide 47
Currents for Circuits with Balanced Load (Delta-connected)
⚫

## Slide 48: Delta(Δ)-Star(Y) conversion and Star-Delta conversion
The formulas for delta-star conversion, using resistance
The formulas for star-delta conversion, using resistance, are

## Slide 49: For impedance conduction
The formulas for delta-star conversion, using impedances.
The formulas for delta-star conversion, using impedance, are

## Slide 50: Thank You
.